## Slide 1: Data Processing of Resting-State fMRI (Part 3): DPARSF Advanced Edition
<number>
YAN Chao-Gan
严超赣
Ph. D.
ycg.yan@gmail.com
State Key Laboratory of Cognitive Neuroscience and Learning,
Beijing Normal University, China

## Slide 2: Outline
Overview
New Functions
Template Parameters
<number>

## Slide 3: DPARSF
(Yan and Zang, 2010)

## Slide 4
<number>
Based on Matlab, SPM, REST, MRIcroN’s dcm2nii

## Slide 5: DPARSF Basic Edition
<number>
Type in “DPARSF” to start
Simple but not flexible
Strong parameters checking and wrong processing prevention

## Slide 6: DPARSF Advanced Edition
<number>
Type in “DPARSFA” to start
The processing steps can be freely skipped or combined
The processing can be start with any Starting Directory Name
Support ReHo, ALFF/fALFF and Functional Connectivity calculation in individual space
The masks or ROI files would be resampled automatically if the dimension mismatched the functional images.

## Slide 7: DPARSF Advanced Edition
<number>
The masks or ROI files in standard space can be warped into individual space by using the parameters estimated in unified segmentaion
Support VBM analysis by checking "Segment" only
Support reorientation interactively if the images in a bad orientation
Support define regions of interest interactively based on the participant's T1 image in individual space

## Slide 8: Outline
Overview
New Functions
Template Parameters
<number>

## Slide 9: Same as DPARSF Basic Edition: Please refer to Data Processing Multimedia Course (Part 1)
Working Dir where stored Starting Directory (e.g., FunRaw)
Number of time points
Detected participants
TR
<number>

## Slide 10: Template Parameters
Standard Steps Calculate in Original Space (Warp) Intraoperative Processing VBM
<number>

## Slide 11: Same as DPARSF Basic Edition: Please refer to Data Processing Multimedia Course (Part 1)
DICOM to NIfTI, based on MRIcroN’s dcm2nii
Remove several first time points
<number>
Slice Timing

## Slide 12: Same as DPARSF Basic Edition: Please refer to Data Processing Multimedia Course (Part 1)
<number>
Total slice number
Reference slice: slice acquired in the middle time of each TR
Slice order: 1:2:33,2:2:32 (interleaved scanning)
Realign
T1 DICOM files to NIfTI

## Slide 13: Coregister T1 image to functional space
<number>
A hidden step in normalization by using T1 image segmentation in DPARSF Basic Edition

## Slide 14: Normalize
Methods:
Normalize by using EPI templates
Normalize by using T1 image unified segmentation
Structural image was coregistered to the mean functional image after the motion correction
The transformed structural image was then segmented into gray matter, white matter, cerebrospinal fluid by using a unified segmentation algorithm
Normalize: the motion corrected functional volumes were spatially normalized to the MNI space using the normalization parameters estimated during unified segmentation (*_seg_sn.mat)

## Slide 15: Coregister T1 image to functional space
<number>
Source Image: T1 image
Reference Image: mean*.img generated in realign step.
If there is no mean*.img generated in realign step DPARSFA will generate a mean functional image automatically.

## Slide 16: Reorient Interactively
<number>
Reorientat interactively if the images in a bad orientation

## Slide 17
<number>

## Slide 18
<number>

## Slide 19: Reorient Interactively
<number>
The reorientation effects on coregisted T1 image and realigned (if realign is performed) functional images.

## Slide 20: Segment
<number>
A hidden step in normalization by using T1 image segmentation in DPARSF Basic Edition
Now it can be used in VBM alone.

## Slide 21: By-Product: VBM
GM in original space
WM in original space
GM in normalized space
Modulated GM in normalized space
CSF in original space
Matrix to warp image from individual space to MNI space
Matrix to warp image from MNI space to individual space

## Slide 22
Same as DPARSF Basic Edition: Please refer to Data Processing Multimedia Course (Part 1)
<number>
Bounding box
Normalize by using EPI templates
Voxel size
Normalize

## Slide 23: Normalize by using T1 image unified segmentation
<number>
Parameter File: *_seg_sn.mat generated in unified segmentation
Images to Write: Functional images (e.g., r*.img if realign is performed)

## Slide 24
Same as DPARSF Basic Edition: Please refer to Data Processing Multimedia Course (Part 1)
<number>
Delete files before normalization to save disk space. The raw data (FunRaw and T1Raw) will be reserved.

## Slide 25
<number>
FWHM kernel
Unchecked: The following processing steps are based on Data without smooth (e.g., ReHo)
Checked: The following processing steps are based on Data with smooth (e.g., ALFF, fALFF, Funtional Connectivity)
Smooth

## Slide 26
Same as DPARSF Basic Edition: Please refer to Data Processing Multimedia Course (Part 1)
<number>
Remove linear trend
Ideal band pass filter
Delete detrented files to save disk space. Do not select this option if fALFF is wanted.

## Slide 27
<number>
Mask
Default mask: SPM5 apriori mask (brainmask.nii) thresholded at 50%.
User-defined mask
If the resolution of default mask or user-defined mask is different from the functional data:
(1) In DPARSF (Basic Edition): Error
(2) In DPARSF (Advanced Edition): resample the masks automatically

## Slide 28
Mask Resample
0 – Nearest Neighbor
<number>
Default mask (BrainMask_05_91x109x91.img, voxel size: 2x2x2) or user-defined mask
The first time point of functional images
{Work Dir}\Masks

## Slide 29
Same as DPARSF Basic Edition: Please refer to Data Processing Multimedia Course (Part 1)
<number>
ReHo Calculation
ALFF/fALFF Calculation

## Slide 30
<number>
rp*.txt
CsfMask_07_61x73x61.img
BrainMask_05_61x73x61.img
WhiteMask_09_61x73x61.img
Regress out nuisance Covariates

## Slide 31
<number>
Regress out nuisance Covariates
If the resolution of masks is different from the functional data:
(1) In DPARSF (Basic Edition): Error
(2) In DPARSF (Advanced Edition): resample the masks automatically (based on *_91x109x91.img, voxel size: 2x2x2)

## Slide 32
Extract ROI time courses (also for ROI-wise Functional Connectivity)
<number>
Same as DPARSF Basic Edition: Please refer to Data Processing Multimedia Course (Part 1)
Functional Connectivity (voxel-wise)
Define ROI

## Slide 33
<number>
Define ROI Interactively

## Slide 34
<number>
0 means define ROI Radius for each ROI seperately

## Slide 35
<number>

## Slide 36
<number>
Extract AAL time courses
If the resolution of AAL mask is different from the functional data:
(1) In DPARSF (Basic Edition): Error
(2) In DPARSF (Advanced Edition): resample the masks automatically (based on aal.nii, voxel size: 1x1x1)

## Slide 37
<number>
Warp Masks into Individual Space
Parameter File: *_seg_inv_sn.mat stored in "T1ImgSegment" directory which is estimated in the T1 image unified segmentation

## Slide 38
<number>
Warp Masks into Individual Space
Images to Write:
1. The calculation mask (also regarded as the whole-barin mask, e.g. the "Default mask")
2. The covariates masks in regressing out covariates
3. The ROI masks used in Functional Connectivity or Extracting ROI Time courses
4. The AAL mask used in Extracting AAL time courses (90 regions)

## Slide 39
<number>
Warp Masks into Individual Space
Stored in {Work Dir}\Masks
The ROIs defined Interactively will NOT be warped since they are defined in the INDIVIDUAL SPACE

## Slide 40
<number>
Starting Directory Name
If you do not start with raw DICOM images, you need to specify the Starting Directory Name.
E.g. "FunImgARW" means you start with images which have been slice timed, realigned and normalized.
Abbreviations:
A - Slice Timing
R - Realign
W - Normalize
S - Smooth
D - Detrend
F - Filter
C - Covariates Removed

## Slide 41: Outline
Overview
New Functions
Template Parameters
<number>

## Slide 42: Template Parameters
<number>
Standard Steps
Calculate in Original Space (Warp)
Intraoperative Processing
VBM

## Slide 43: Standard Steps
<number>

## Slide 44: DPARSF's standard procedure
Convert DICOM files to NIFTI images.
Remove First 10 Time Points.
Slice Timing.
Realign.
Normalize.
Smooth (optional).
Detrend.
Filter.
Calculate ReHo, ALFF, fALFF (optional).
Regress out the Covariables (optional).
Calculate Functional Connectivity (optional).
Extract AAL or ROI time courses for further analysis (optional).
Please refer to Data Processing Multimedia Course (Part 1)

## Slide 45: Calculate in Original Space (Warp)
<number>
Segment to produce *_seg_inv_sn.mat stored in "T1ImgSegment" directory
Warp masks into Individual space
The calculation is performed in individual space

## Slide 46: Intraoperative Processing
<number>
No realign since there is no head motion. DPARSFA will generate the mean functional images automatically.
Reorient interactively since T1 images are in a bad orientation. Reorientation effects on coregistered T1 image and functional images after slice timing correction
Define ROI Interactively since normalization is not performed

## Slide 47: VBM
<number>
Only Segment checkbox is checked
Define the Starting Directory Name as T1Raw

## Slide 48: Further Help
www.restfmri.net
Further questions:
<number>

## Slide 49: Thanks to
DONG Zhang-Ye
GUO Xiao-Juan
HE Yong
LONG Xiang-Yu
SONG Xiao-Wei
YAO Li
ZANG Yu-Feng
ZHANG Han
ZHU Chao-Zhe
ZOU Qi-Hong
ZUO Xi-Nian
……
All the group members!
SPM Team: Wellcome Department of Imaging Neuroscience, UCL
MRIcroN Team: Chris RORDEN
Xjview Team: CUI Xu
……

## Slide 50: Thanks for your attention!
<number>