## Slide 1: Data Processing Assistant for Resting-State fMRI: Speed Up Your Data Analysis
YAN Chao-Gan
严超赣
Ph. D.
ycg.yan@gmail.com
State Key Laboratory of Cognitive Neuroscience and Learning,
Beijing Normal University, China
Course: Data Processing of Resting-State fMRI (Part 1)

## Slide 2: Outline
Overview
Data Preparation
Preprocess
ReHo, ALFF, fALFF Calculation
Functional Connectivity
Utilities
Notes: <number>
<footer>
<header>
<date/time>

## Slide 3: Overview
Based on Matlab, SPM, REST, MRIcroN’s dcm2nii
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: DPARSF's standard procedure
Convert DICOM files to NIFTI images.
Remove First 10 Time Points.
Slice Timing.
Realign.
Normalize.
Smooth (optional).
Detrend.
Filter.
Calculate ReHo, ALFF, fALFF (optional).
Regress out the Covariables (optional).
Calculate Functional Connectivity (optional).
Extract AAL or ROI time courses for further analysis (optional).
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5: Outline
Overview
Data Preparation
Preprocess
ReHo, ALFF, fALFF Calculation
Functional Connectivity
Utilities
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: Data preparation
Arrange the information of the subjects
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: Data preparation
Information of subjects
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: Data preparation
Arrange the information of the subjects
Arrange the MRI data of the subjects
Functional MRI data
Structural MRI data
DTI data
Notes: <number>
<footer>
<header>
<date/time>

## Slide 9
被试信息整理
原始数据整理
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10
Sort DICOM data
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11
IMA
dcm
none
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12: Data preparation
Arrange each subject's fMRI DICOM images in one directory, and then put them in "FunRaw" directory under the working directory.
Subject 1’s DICOM files
FunRaw directory, please name as this
Subject 1’s directory
Working directory
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: Data preparation
Arrange each subject's T1 DICOM images in one directory, and then put them in “T1Raw" directory under the working directory.
Subject 1’s DICOM files
T1Raw directory, please name as this
Subject 1’s directory
Working directory
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14: Data preparation
Set the parameters in DPARSF
Set the working directory
Set the time points (volumes)
The detected subjects’ ID
Set the TR
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15: Outline
Overview
Data Preparation
Preprocess
ReHo, ALFF, fALFF Calculation
Functional Connectivity
Utilities
Notes: <number>
<footer>
<header>
<date/time>

## Slide 16: Preprocess
DICOM -> NIFTI
Remove First 10 Time Points
Slice Timing
Realign
Normalize
Smooth
Detrend
Filter: 0.01-0.08
Notes: <number>
<footer>
<header>
<date/time>

## Slide 17: DICOM->NIFTI
MRIcroN’s dcm2niigui
SPM5’s DICOM Import
Notes: <number>
<footer>
<header>
<date/time>

## Slide 18: DICOM->NIFTI
DPARSF
Notes: <number>
<footer>
<header>
<date/time>

## Slide 19: Preprocess
DICOM -> NIFTI
Remove First 10 Time Points
Slice Timing
Realign
Normalize
Smooth
Detrend
Filter: 0.01-0.08
Notes: <number>
<footer>
<header>
<date/time>

## Slide 20: Remove First 10 Time Points
DPARSF
Notes: <number>
<footer>
<header>
<date/time>

## Slide 21: Preprocess
DICOM -> NIFTI
Remove First 10 Time Points
Slice Timing
Realign
Normalize
Smooth
Detrend
Filter: 0.01-0.08
Notes: <number>
<footer>
<header>
<date/time>

## Slide 22: Slice Timing
Why?
Notes: <number>
<footer>
<header>
<date/time>

## Slide 23: Slice Timing
Why?
Huettel et al., 2004
Notes: <number>
<footer>
<header>
<date/time>

## Slide 24: Slice Timing
1:2:25,2:2:24
25
2
2-(2/25)
25
Notes: <number>
<footer>
<header>
<date/time>

## Slide 25: Slice Timing
Notes: <number>
<footer>
<header>
<date/time>

## Slide 26: Slice Timing
DPARSF
1:2:25,2:2:24
Notes: <number>
<footer>
<header>
<date/time>

## Slide 27: Slice Timing
If you start with NIFTI images (.hdr/.img pairs) before slice timing, you need to arrange each subject's fMRI NIFTI images in one directory, and then put them in "FunImg" directory under the working directory.
FunImg directory, please name as this
Notes: <number>
<footer>
<header>
<date/time>

## Slide 28: Preprocess
DICOM -> NIFTI
Remove First 10 Time Points
Slice Timing
Realign
Normalize
Smooth
Detrend
Filter: 0.01-0.08
Notes: <number>
<footer>
<header>
<date/time>

## Slide 29: Realign
Why?
Notes: <number>
<footer>
<header>
<date/time>

## Slide 30: Realign
Notes: <number>
<footer>
<header>
<date/time>

## Slide 31: Realign
DPARSF
Notes: <number>
<footer>
<header>
<date/time>

## Slide 32: Realign
Check head motion:
Excluding Criteria: 2.5mm and 2.5 degree
None
Excluding Criteria: 2.0mm and 2.0 degree
Sub_013
Excluding Criteria: 1.5mm and 1.5 degree
Sub_013
Excluding Criteria: 1.0mm and 1.0 degree
Sub_007
Sub_012
Sub_013
Sub_017
Sub_018
Notes: <number>
<footer>
<header>
<date/time>

## Slide 33: Preprocess
DICOM -> NIFTI
Remove First 10 Time Points
Slice Timing
Realign
Normalize
Smooth
Detrend
Filter: 0.01-0.08
Notes: <number>
<footer>
<header>
<date/time>

## Slide 34: Normalize
Why?
Huettel et al.,
2004
Notes: <number>
<footer>
<header>
<date/time>

## Slide 35: Normalize
Methods:
I. Normalize by using EPI templates
II. Normalize by using T1 image unified segmentation
Notes: <number>
<footer>
<header>
<date/time>

## Slide 36
mean_name.img
r*.img
EPI.nii
-90 -126 -72; 90 90 108
3 3 3
Notes: <number>
<footer>
<header>
<date/time>

## Slide 37: Normalize I
Notes: <number>
<footer>
<header>
<date/time>

## Slide 38: Normalize
Methods:
Normalize by using EPI templates
Normalize by using T1 image unified segmentation
Structural image was coregistered to the mean functional image after the motion correction
The transformed structural image was then segmented into gray matter, white matter, cerebrospinal fluid by using a unified segmentation algorithm
Normalize: the motion corrected functional volumes were spatially normalized to the MNI space using the normalization parameters estimated during unified segmentation (*_seg_sn.mat)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 39: Normalize II: Coregister
mean_name.img
T1.img
Notes: <number>
<footer>
<header>
<date/time>

## Slide 40: Normalize II:
T1_Coregisted.img
Light Clean
ICBM space template – East Asian brains
– European brains
Notes: <number>
<footer>
<header>
<date/time>

## Slide 41: Normalize II: Segment
New “Segment”
Notes: <number>
<footer>
<header>
<date/time>

## Slide 42: Normalize II:
New “Normalize: Write”
New “Subject”
name_seg_sn.mat
-90 -126 -72; 90 90 108
3 3 3
r*.img
Notes: <number>
<footer>
<header>
<date/time>

## Slide 43: Normalize
DPARSF
T1 Data should be arranged in T1Raw or T1Img (co*.img) directory!
Delete files before normalization:
raw NIfTI files, slice timing files, realign files.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 44: Normalize
Check Normalization with DPARSF
{WROKDIR}\PicturesForChkNormalization
Notes: <number>
<footer>
<header>
<date/time>

## Slide 45: Preprocess
DICOM -> NIFTI
Remove First 10 Time Points
Slice Timing
Realign
Normalize
Smooth
Detrend
Filter: 0.01-0.08
Notes: <number>
<footer>
<header>
<date/time>

## Slide 46: Smooth
Why?
Reduce the effects of the bad normalization
…
Notes: <number>
<footer>
<header>
<date/time>

## Slide 47: Smooth
w*.img
FWHM kernel
Notes: <number>
<footer>
<header>
<date/time>

## Slide 48: Smooth
DPARSF
ALFF, fALFF, Funtional Connectivity: Data with smooth
ReHo:
Data without smooth
Without former steps: Data arranged in FunImgNormalized directory.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 49: Preprocess
DICOM -> NIFTI
Remove First 10 Time Points
Slice Timing
Realign
Normalize
Smooth
Detrend
Filter: 0.01-0.08
Notes: <number>
<footer>
<header>
<date/time>

## Slide 50: Detrend
Notes: <number>
<footer>
<header>
<date/time>

## Slide 51: Preprocess
DICOM -> NIFTI
Remove First 10 Time Points
Slice Timing
Realign
Normalize
Smooth
Detrend
Filter: 0.01-0.08
Notes: <number>
<footer>
<header>
<date/time>

## Slide 52: 滤波
Why?
Low frequency (0.01–0.08 Hz) fluctuations (LFFs) of the resting-state fMRI signal were of physiological importance. (Biswal et al., 2005)
LFFs of resting-state fMRI signal were suggested to reflect spontaneous neuronal activity (Logothetis et al., 2001; Lu et al., 2007).
Biswal B, Yetkin FZ, Haughton VM, Hyde JS (1995) Functional connectivity in the motor cortex of resting human brain using echo-planar MRI. Magn Reson Med 34: 537–541.
Logothetis NK, Pauls J, Augath M, Trinath T, Oeltermann A (2001) Neurophysiological investigation of the basis of the fMRI signal. Nature 412: 150–157.
Lu H, Zuo Y, Gu H, Waltz JA, Zhan W, et al. (2007) Synchronized delta oscillations correlate with the resting-state functional MRI signal. Proc Natl Acad Sci U S A 104: 18265–18269.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 53: Filter
Notes: <number>
<footer>
<header>
<date/time>

## Slide 54: Detrend and Filter
DPARSF
If you want to calculate fALFF, please do not delete the detrended files
Without former steps: Data arranged in FunImgNormalized or FunImgNormalizedSmoothed directory.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 55: Outline
Overview
Data Preparation
Preprocess
ReHo, ALFF, fALFF Calculation
Functional Connectivity
Utilities
Notes: <number>
<footer>
<header>
<date/time>

## Slide 56: ReHo (Regional Homogeneity)
Note: Please do not smooth your data in preprocessing, just smooth your data after ReHo calculation.
Zang et al., 2004
Zang YF, Jiang TZ, Lu YL, He Y, Tian LX (2004) Regional homogeneity approach to fMRI data analysis. Neuroimage 22: 394–400.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 57: ReHo
If the resolution of your data is not 61*61*73, please resample your mask file at first.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 58: Data Resample
Choose one of your functional image. e.g. your normalized functional image or image after Detrend and Filter.
Choose the mask file or ROI definition file. e.g. BrainMask_05_61x73x61.img
Resample Mask
Resample other kind of data
Notes: <number>
<footer>
<header>
<date/time>

## Slide 59
Data Resample
Notes: <number>
<footer>
<header>
<date/time>

## Slide 60
Data Resample
0 – Nearest Neighbor
1 – Trilinear
2- 2nd degree b-spline
Notes: <number>
<footer>
<header>
<date/time>

## Slide 61: ReHo
Please ensure the resolution of your own mask is the same as your functional data.
Without former steps: Data arranged in FunImgNormalizedDetrendedFiltered
directory.
DPARSF
Get the smReHo -1 or mReHo - 1 data for one sample T test.
Smooth the mReHo results. The FWHM kernel is the same as set in the smooth step.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 62
Zang et al., 2007
Zang YF, He Y, Zhu CZ, Cao QJ, Sui MQ, et al. (2007) Altered baseline brain activity in children with ADHD revealed by resting-state functional MRI. Brain Dev 29: 83–91.
ALFF (Amplitude of Low Frequency Fluctuation )
Notes: <number>
<footer>
<header>
<date/time>

## Slide 63: fALFF (fractional ALFF )
Zou et al., 2008
Zou QH, Zhu CZ, Yang Y, Zuo XN, Long XY, et al. (2008) An improved approach to detection of amplitude of low-frequency fluctuation (ALFF) for resting-state fMRI: fractional ALFF. J Neurosci Methods 172: 137-141.
PCC: posterior cingulate cortex
SC: suprasellar cistern
Notes: <number>
<footer>
<header>
<date/time>

## Slide 64: ALFF
fALFF: DO NOT filter!
Notes: <number>
<footer>
<header>
<date/time>

## Slide 65: ALFF and fALFF
Without former steps: Data arranged in FunImgNormalizedSmoothedDetrendedFiltered
or FunImgNormalizedSmoothedDetrended directory.
Please ensure the resolution of your own mask is the same as your functional data.
DPARSF
Get the mALFF - 1 or (mfALFF - 1) data for one sample T test.
Please DO NOT delete the detrended files before filter. DPARSF will calculated the fALFF based on data before filter.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 66: Outline
Overview
Data Preparation
Preprocess
ReHo, ALFF, fALFF Calculation
Functional Connectivity
Utilities
Notes: <number>
<footer>
<header>
<date/time>

## Slide 67: Regress out nuisance covariates
Head motion parameters: rp_name.txt
Global mean signal
White matter signal
Cerebrospinal fluid signal
Notes: <number>
<footer>
<header>
<date/time>

## Slide 68
Extract
Covariates
Notes: <number>
<footer>
<header>
<date/time>

## Slide 69
Extract
Covariates
Notes: <number>
<footer>
<header>
<date/time>

## Slide 70
Extract
Covariates
Notes: <number>
<footer>
<header>
<date/time>

## Slide 71
Extract
Covariates
Notes: <number>
<footer>
<header>
<date/time>

## Slide 72
Extract
Covariates
Notes: <number>
<footer>
<header>
<date/time>

## Slide 73
Extract
Covariates
Extract one subject’s Covariates
Notes: <number>
<footer>
<header>
<date/time>

## Slide 74
Extract
Covariates
Extract multi subjects’ Covariates
Notes: <number>
<footer>
<header>
<date/time>

## Slide 75
Extract
Covariates
Notes: <number>
<footer>
<header>
<date/time>

## Slide 76
Extract
Covariates
Notes: <number>
<footer>
<header>
<date/time>

## Slide 77: Regress out nuisance Covariates
Extract Covariates
Head motion parameters: rp_name.txt
Global mean signal
White matter signal
Cerebrospinal fluid signal
Combine the covariates for future using in REST
RPCov=load('rp_name.txt');
BCWCov=load('ROI_FCMap_name.txt');
Cov=[RPCov,BCWCov];
save('Cov.txt', 'Cov', '-ASCII', '-DOUBLE','-TABS');
Notes: <number>
<footer>
<header>
<date/time>

## Slide 78
Regress out
Covariates
Notes: <number>
<footer>
<header>
<date/time>

## Slide 79
Extract
Covariates
CovList.txt:
Covariables_List:
X:\Process\Sub3Cov.txt
X:\Process\Sub2Cov.txt
X:\Process\Sub1Cov.txt
CovList.txt:
Notes: <number>
<footer>
<header>
<date/time>

## Slide 80
Without former steps: Data arranged in FunImgNormalizedDetrendedFiltered
or FunImgNormalizedSmoothedDetrendedFiltered
directory.
rp*.txt
DPARSF
CsfMask_07_61x73x61.img
BrainMask_05_61x73x61.img
Regress out nuisance Covariates
WhiteMask_09_61x73x61.img
Notes: <number>
<footer>
<header>
<date/time>

## Slide 81
Without former steps: Data arranged in FunImgNormalizedDetrendedFiltered
or FunImgNormalizedSmoothedDetrendedFiltered
directory.
DPARSF
Regress out Covariates
Notes: <number>
<footer>
<header>
<date/time>

## Slide 82
Regress out Covariates
Notes: <number>
<footer>
<header>
<date/time>

## Slide 83
Please ensure the resolution of your ROI file is the same as your functional data.
Regress out Covariates
Notes: <number>
<footer>
<header>
<date/time>

## Slide 84
Without former steps: Data arranged in FunImgNormalizedDetrendedFiltered
or FunImgNormalizedSmoothedDetrendedFiltered
directory.
DPARSF
Regress out Covariates
Notes: <number>
<footer>
<header>
<date/time>

## Slide 85: Regress out Covariates
Arrange each subject's covariates (each covariate in one column) in one directory, and then put them in “RealignParameter" directory under the working directory.
Each covariate in one column
RealignParameter directory, please name as this
Subject 1’s directory
Working directory
Notes: <number>
<footer>
<header>
<date/time>

## Slide 86: Functional Conncetivity
Voxel-wise
ROI-wise
r=0.36
Notes: <number>
<footer>
<header>
<date/time>

## Slide 87
Voxel-wise
Notes: <number>
<footer>
<header>
<date/time>

## Slide 88
Voxel-wise
Please ensure the resolution of your ROI file is the same as your functional data.
SeedList.txt:
Seed_Time_Course_List:
X:\Process\Sub3Seed.txt
X:\Process\Sub2Seed.txt
X:\Process\Sub1Seed.txt
Notes: <number>
<footer>
<header>
<date/time>

## Slide 89
Voxel-wise
Notes: <number>
<footer>
<header>
<date/time>

## Slide 90
Voxel-wise
Notes: <number>
<footer>
<header>
<date/time>

## Slide 91
Voxel-wise
Notes: <number>
<footer>
<header>
<date/time>

## Slide 92
Voxel-wise
Notes: <number>
<footer>
<header>
<date/time>

## Slide 93
Voxel-wise
CovList.txt
CovList.txt:
Covariables_List:
X:\Process\Sub6Cov.txt
X:\Process\Sub5Cov.txt
X:\Process\Sub4Cov.txt
X:\Process\Sub3Cov.txt
X:\Process\Sub2Cov.txt
X:\Process\Sub1Cov.txt
Notes: <number>
<footer>
<header>
<date/time>

## Slide 94
ROI-wise
Notes: <number>
<footer>
<header>
<date/time>

## Slide 95
ROI-wise
Notes: <number>
<footer>
<header>
<date/time>

## Slide 96
ROI-wise
CovList.txt
CovList.txt:
Covariables_List:
X:\Process\Sub6Cov.txt
X:\Process\Sub5Cov.txt
X:\Process\Sub4Cov.txt
X:\Process\Sub3Cov.txt
X:\Process\Sub2Cov.txt
X:\Process\Sub1Cov.txt
Notes: <number>
<footer>
<header>
<date/time>

## Slide 97: Functional Connectivity
Without former steps: Data arranged in FunImgNormalizedDetrendedFilteredCovremoved
or FunImgNormalizedSmoothedDetrendedFilteredCovremoved directory.
Please ensure the resolution of your own mask is the same as your functional data.
DPARSF
Notes: <number>
<footer>
<header>
<date/time>

## Slide 98
Functional Connectivity
Notes: <number>
<footer>
<header>
<date/time>

## Slide 99: Functional Connectivity
You will get the Voxel-wise functional connectivity results of each ROI in {working directory}\Results\FC:
zROI1FCMap_Sub_001.img
zROI2FCMap_Sub_001.img
For ROI-wise results, please see Part Utilities: Extract ROI time courses.
DPARSF
Notes: <number>
<footer>
<header>
<date/time>

## Slide 100: Outline
Overview
Data Preparation
Preprocess
ReHo, ALFF, fALFF Calculation
Functional Connectivity
Utilities
Notes: <number>
<footer>
<header>
<date/time>

## Slide 101: Extract ROI time courses
Without former steps: Data arranged in FunImgNormalizedDetrendedFilteredCovremoved
or FunImgNormalizedSmoothedDetrendedFilteredCovremoved directory.
DPARSF
Notes: <number>
<footer>
<header>
<date/time>

## Slide 102
Extract ROI time courses
Notes: <number>
<footer>
<header>
<date/time>

## Slide 103: Extract ROI time courses
Results in {working direcotry}\FunImgNormalizedDetrendedFilteredCovremoved_RESTdefinedROITC:
DPARSF
Sub_001_ROITimeCourses.txt: Time courses, each column represent a time course of one ROI.
Sub_001_ResultCorr.txt: ROI-wise Functional Connectivity
Notes: <number>
<footer>
<header>
<date/time>

## Slide 104: Extract AAL time courses
Without former steps: Data arranged in FunImgNormalizedDetrendedFilteredCovremoved
or FunImgNormalizedSmoothedDetrendedFilteredCovremoved directory.
DPARSF
Notes: <number>
<footer>
<header>
<date/time>

## Slide 105: Extract AAL time courses
Results in {working direcotry}\FunImgNormalizedDetrendedFilteredCovremoved_AALTC:
DPARSF
Sub_001_AALTC.mat: Time courses of each AAL region.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 106: Change prefix of Images
Normalization by using T1 image segmentation: co*.img
Realign without Slice Timeing: a*.img
DPARSF
Notes: <number>
<footer>
<header>
<date/time>

## Slide 107: Change prefix of Images
Normalization by using T1 image segmentation: co*.img
DPARSF
a
a*.img -> ra*.img
ra
Notes: <number>
<footer>
<header>
<date/time>

## Slide 108: Save and Load Parameters
Save parameters to *.mat
DPARSF
Load parameters from *.mat
Notes: <number>
<footer>
<header>
<date/time>

## Slide 109: Further Help
www.restfmri.net
Further questions:
Further professional data analysis service:
Brain Imaging Data Analysis and Consultation Section (BIDACS)
bidacs@gmail.com
Notes: <number>
<footer>
<header>
<date/time>

## Slide 110: Thanks to
DONG Zhang-Ye
GUO Xiao-Juan
HE Yong
LONG Xiang-Yu
SONG Xiao-Wei
YAO Li
ZANG Yu-Feng
ZHANG Han
ZHU Chao-Zhe
ZOU Qi-Hong
ZUO Xi-Nian
……
All the group members!
SPM Team: Wellcome Department of Imaging Neuroscience, UCL
MRIcroN Team: Chris Rorden
……

## Slide 111
Thanks for your attention!